Hardware

Standard RCA1802 clocked at 2Mhz.
64k of RAM
A simplified UART for keyboard/screen I/O

Keyboard

Key strobe is at EF1 (set when a key is available)
The key is read from port 1, reading this clears the strobe.
Keys used are CR (13) BS(8) and the normal ASCII character set 32-127

Display

Ready to Transmit is at EF2 (set when the buffer is empty)
The character is written to port 2, which starts the data transfer.

The display can be any size, but will probably be 32 x 16. Characters accepted are CR, 32-127 ASCII and Backspace (which is printed as ^H)

Program Storage

Program lines are numbered 0-255. Each line can be up to 128 characters in length. Lines occupy 32k of RAM memory, from 8000-FFFF. Each line is at its line number * 128

shr
ori	80	; if can arrange for DF to be set can use RSHR here.
phi	r9
ldi	0
rshr

Initial expression

constants
variables [A-Z]
+/- operators (add * / & | ^ > < = if space) need to have some form of testing. No unary ?